# Preface
This document lists many examples of VDF-files and accompanying explanations which can helpful for your own application. It starts with simple examples of changing a single setting, shows advanced use with if-else like assignments and ends with how to redefine your pump profile.

The easy way to check what can be adapted is to look into the SMB tab and go through the loop input sections:
Constraints
They are checked in other parts of AAPS and are out of reach. However, when you change some other setting these hard limits are not checked by the emulator. that means fi you feel you need to lift those hard limits in your private version of AAPS you can run the mulator with larger values to find your personal hard limit.
Glucose status (called glucose_status)
These data come from the CGM, be it directly, after smoothing or further processing like bg-deltas or bg-acceleration. They should not be adapted.
Current temp

IOB data (called iob_data)
The calculation of IOB is not part of the code which was migrated to the emulator and is therefore out of scope.
Profile (called profile)
Most of the AAPS settings are part of this AAPS profile. Do not get confused with the pump profile, that is just an unlucky wording. You can see all the possible items listed here.
Meal data (called meal_data)
The calculation of IOB is not part of the code which was migrated to the emulator and is therefore out of scope.
Autosense data (called autosense_data)
The calculation of IOB is not part of the code which was migrated to the emulator and is therefore out of scope.

# Layout and general hints
The VDF-file ebntries have 4 logical groups or columns:	You can think of it as a spreadsheet:
1. group name like profile	a column heading
2. element within the group like min_bg	a row heading
3. assigned new value like 95	a cell content like value or formula
4. optionally comment field like ### my text	a comment attached to the cell
The examples given above will look like this:
profile	min_bg	95	### my text
The examples may be used via copy/paste. In your own typing be careful with the single quote character like below in profile['min_bg']. There are other characters that look similar like a backwards single quote. All those lead to errors. If in doubt copy it from here.
#### The group temp
This is a special group besides profile etc. and holds your own interim variables with your own names. Especially when you create long and comlex expressions it can hold interim results and simplify debugging. This is useful when you need several complex expressions in your VDF. In the example to the right the variable “var1” was added with a value of 10 and later referred to in cell “B4”. In VDF formluation it looks like this:
temp	var1	10	### interim value
profile	min_bg	95	### new lower target, fixed
profile	max_bg	profile['min_bg'] + temp['var1']	### new upper target, expression

# Profile – adapting settings in regular AAPS
#### Adapting targets
This a very frequent situation. Let us start with alternative methods how to set a lower target:
profile	min_bg	95	### a simple, fixed assignment

This will set the lower target to 95 no matter what it was in the master run. It is your responsibilty to ensure this is not higher than the upper target value.

If we want to be more advanced we may use an expression rather than a fixed value like this:

profile	min_bg	profile['min_bg'] + 10	### a simple, relative assignment

This will set the lower target to10mg/dl higher than it was in the master run. The expression profile['min_bg'] refers to the current value and this formalism with square brackets and single quotes can be used in anlogy for all other current settings.
If we want to be careful not to exceed 99mg/dl as our lower target we can expand it further:
profile	min_bg	min(99,profile['min_bg']+10)	### use the python function ”min”

Varying the upper target works in analogy. There is one special case, namely mimicing a TempTarget. To achieve that we need to define lower and upper targets, ensure they have the same value and set the flag for the target being a TempTarget. It goes like this:
profile	min_bg	min(99,profile['min_bg']+10)	### use the python function ”min”
profile	max_bg	profile['min_bg']	### copy from lower target
profile	temptargetSet	True	### enable the flag

You may have wondered why we do not declare the intended target_bg likewise and directly. In fact that is always calculated as average of min_bg and max_bg inside AAPS and the emulator anyway. If we have a TempTarget active in the master run we may simply disable it with a 1-liner:
profile	temptargetSet	False	### disable the flag

#### Adapting ISF, CR and basal
In the previous section er learned that there was no command to directly set a TempTarget. Likewise there is no command to directly set a percentage change of the profile but we can set them individually. To make the case more challenging and building on what we did for the targets let us assume we want to mimic a 10% increase in resistance. Here is the VDF that does it:
profile	sens	profile['sens']	* 1.1	### numerically increase ISF by 10%
profile	carb_ratio	profile['carb_ratio'] / 1.1	### numerically reduce CR by 10%
profile	current_basal	profile['current_basal']*1.1	### numerically increase basal by 10%

Of cause we can just set one of them on its own. Let us assume we want to modify ISF based on delta:
temp	slope	glucose_status['delta']	### holds BG delta
profile	sens	profile['sens'] - temp['slope']	### stronger if BG climbs, weaker if BG falls

Now let us assume we only want such an adaptation if BG was flat before. As flat we define the change in BG slope was recently less than ± 3mg/dl when comparing delta and short_avgdelta. In the VDF such logical tests result in “1” if True and “0” if False which makes it possible to get different results for different conditions. Have a look:
temp	acce	glucose_status['delta']-glucose_status['short_avgdelta']	### estimated acceleration
temp	OK	abs(temp['acce']) > 3	### “1” if acce > ± 3mg/dl, “0” else
temp	slope	glucose_status['delta'] * temp['OK']	### holds BG delta if True, “0” else
profile	sens	profile['sens'] - temp['slope']	### stronger if BG climbs, weaker if BG falls

In cases of such complex definitions it is a must to check that these expressions evaluate as intended. The LOG-file echos every result of the VDF-file line by line. Here are extracts from the LOG-file showing the 3 possible results:
loop execution in row=7635 of logfile l:\not_me\Norbert\AndroidAPS._2022-04-20_10-31-49_.2.zip at= 2022-04-20T09:05:52.560Z
appended new entry to temp with acce=-2.3899999999999997
appended new entry to temp with OK=False
appended new entry to temp with slope=0
edited old value of 20.159999999999997 in profile with sens=20.159999999999997

loop execution in row=10770 of logfile l:\not_me\Norbert\AndroidAPS._2022-04-20_10-31-49_.2.zip at= 2022-04-20T09:10:33.309Z
appended new entry to temp with acce=3.33
appended new entry to temp with OK=True
appended new entry to temp with slope=2
edited old value of 20.159999999999997 in profile with sens=18.159999999999997
...
loop execution in row=4979 of logfile l:\not_me\Norbert\AndroidAPS._2022-04-20_10-31-49_.3.zip at= 2022-04-20T09:35:17.920Z
appended new entry to temp with acce=3.5600000000000005
appended new entry to temp with OK=True
appended new entry to temp with slope=-5
edited old value of 20.159999999999997 in profile with sens=25.159999999999997

At time 09:05UTC the acceleration is between -3 and +3, so not applicable. The flag variable OK is False and sensititvity is unchanged.
At time 09:10UTC the acceleration is 3.33, so applicable. The flag variable OK is True and sensititvity is reduceded because slope is positive.
At time 09:35UTC the acceleration is 3.56, so applicable. The flag variable OK is True and sensititvity is increased because slope is negative.

This is just a theoretical example of the capabilities. You can try your own approaches. Beleive it or not, many features in autoISF I first developed and tested in VDF before being programmed in the apk itself.

# Adapting a pump profile
In the VDF you can also define your circadiane tables for ISF, CR and basal. You need to pay special attention to the difference between UTC time and your local time zone for the pump. Here is an example for CET (Central European Time):
STAIR_ISF 00:00:00Z 45 ### 01h_C(entral)E(uropean)T(ime) or 02h_CEST
STAIR_ISF 01:00:00Z 44 ###
STAIR_ISF 02:00:00Z 42 ###
...
STAIR_ISF 17:00:00Z 36 ### 18h_CET
STAIR_ISF 18:00:00Z 38 ###
...
STAIR_ISF 22:00:00Z 43 ### 23h_CET
STAIR_ISF 23:00:00Z 44 ### 00h_CET
profile sens STAIR_ISF ###

STAIR_CR 00:00:00Z 8.0 ### 01h_C(entral)E(uropean)T(ime) or 02h_CEST
STAIR_CR 01:00:00Z 7.5 ###
...
STAIR_CR 20:00:00Z 7.5 ###
STAIR_CR 21:00:00Z 8.0 ###
STAIR_CR 22:00:00Z 9.0 ### 23h_CET
STAIR_CR 23:00:00Z 9.0 ### 00h_CET
profile carb_ratio STAIR_CR ###

STAIR_BAS 00:00:00Z 0.41 ### 01h_C(entral)E(uropean)T(ime) or 02h_CEST
STAIR_BAS 01:00:00Z 0.43 ###
STAIR_BAS 02:00:00Z 0.44 ###
STAIR_BAS 03:00:00Z 0.50 ###
...
STAIR_BAS 19:00:00Z 0.75 ### 20h_CET
STAIR_BAS 20:00:00Z 0.75 ###
STAIR_BAS 21:00:00Z 0.60 ###
STAIR_BAS 22:00:00Z 0.45 ### 23h_CET
STAIR_BAS 23:00:00Z 0.43 ### 00h_CET
profile current_basal STAIR_BAS ###

Some lines were omitted in that example for better readability. The lines must be sorted by UTC time. Therefore the first line (winter time) or first two lines (summer time) from your CET based pump definition must be cut off and appended at the end. If your profile ist not fully populated for 24 hours this may also mean you first need to create a pump entry at 01 or 02 hours, respectively.
Before adding anything else to the VDF you should already do a test run and check the LOG file to ensure that the assignmets were correct.
# Handling automations
Regarding automations there are two aspects:
#### How to get rid of automation actions that were present in the master run but may disturb the alternative approach by autoISF
If you used automations to adapt the profile then check the previous page how you would revert the actions and reset the profile to your base defined in the pump.
If you used automations to change targets then consult page 3 of this document which has several examples of how to set targets.When you emulate a longer time window during which the pumps profile has a target change then you can use a method analogeous to the previous page: Here is an example of setting the lower target to 90mg/dl between 02 :00 and 08:00 CET and 95 otherwise.
STAIR_LTG 00:00:00Z 95 ### 01h_C(entral)E(uropean)T(ime) or 02h_CEST
STAIR_LTG 01:00:00Z 90 ###
STAIR_LTG 07:00:00Z 95 ### 08h_CET
STAIR_LTG 23:00:00Z 95 ### 00h_CET
profile min_bg STAIR_LTG ###

The equivalent code word for the higher targets is STAIR_HTG.
#### How to emulate automations inside the emulator
The condition can be checked like we saw in the section about adapting ISF by assigning the result of a logical check to a Temp variable. There are conditions which are only available in the emulator like all the autoISF settings and others only in AAPS. Examples are:
Temp	iobTH5	iob_data['iob'] > 5	### ”1” if IOB>5, ”0” otherwise for checking a threshold
Temp	TTset	profile['temptargetSet']	### ”1” if set, ”0” otherwise
Temp	tGT100	profile['min_bg']	> 100	### ”1” if lower target>100, ”0” otherwise
Temp	bg140	glucose_status['glucose'] > 140	### ”1” if BG>140, ”0” otherwise

For declaring an AND condition you just multiply the related flags, e.g. to check whether TT is set and is above 100:
Temp	TTgt100	temp['TTset'] * temp['tGT100']	### ”1” if TT>100, ”0” otherwise

For declaring an OR condition you add the related flags and check whether it is above 0:
Temp	anyone	temp['iobTH5']+temp['bg140'] > 0	### ”1” if IOB>5 or BG>140, ”0” otherwise

The action of the emulated automation can be any setting the emulator can handle like the examples in the preceeding sections.
# Other special commands
#### STAIR

#### INTERPOL

#### POLYGON

# Changing autoISF settings
All the settings for autoISF are accessible as elements in the group profile. So on tat side there is nothing really new. If however you want to experiment with a new logic or add morfe effects you can test them by appropriate VDF commands.
#### The group new_parameter
This group is used for specific autoISF settings and was introduced to by-pass the internal algo and replace it by your own algo expressed by VDF formulae. So you can redefine any one of the 4 BG effects like this:
new_parameter acce_ISF	my_new_acce_ISF	### insert VDF commands upfront to calculate your own factor
new_parameter bg_ISF	my_new_bg_ISF	### insert VDF commands upfront to calculate your own factor
new_parameter delta_ISF	my_new_delta_ISF	### insert VDF commands upfront to calculate your own factor
new_parameter dura_ISF	my_new_dura_ISF	### insert VDF commands upfront to calculate your own factor

One special trick in this context is to assign a value of “1” which effectively shuts off that individual contribution. That has the same effect as setting the related weight to “0”. For developing your own algo it is helpful to understand the basic results contained in glucose_status:
- glucose	standard APS glucose valid at the time the loop ran
- delta	standard APS delta
- short_avgdelta	standard APS short_avgdelta
- long_avgdelta	standard APS long_avgdelta
- date	time at which the above mentioned glucose was measured
- dura_ISF_minutes	duration of the glucose plateau
- dura_ISF_average	average level of glucose during that plateau window
- slope05	average delta during the last 7.5 minutes calculated from best linear fit
- slope15	average delta during the last 17.5[1] minutes calculated from best linear fit
  [1] Uses interval 0-17.5 as opposed to short_avgdelta which uses 7.5-17.5 minutes
- slope40	average delta during the last 42.5[2] minutes calculated from best linear fit
  [2] Uses interval 0-42.5 as opposed to long_avgdelta which uses 17.5-42.5 minutes
- parabola_fit_correlation	measure of fit quality; “1” is perfect; anything less than “0.9” is disregarded in autoISF
- parabola_fit_minutes	duration of the fit window; min 10m for Libre 1-minute data; min 15m otherwise
- parabola_fit_last_delta	delta between now and 5m ago as derived from the fit formula
- parabola_fit_next_delta	delta between 5m ahead and now as derived from the fit formula
- parabola_fit_a0	fit polynomial coefficient, approximates the current glucose
- parabola_fit_a1	fit polynomial coefficient, current delta, i.e. the tangent to the parabola at this time
- parabola_fit_a2	fit polynomial coefficient, half the acceleration
- bg_acceleration	acceleration derived from fit formula
#### Some theory regarding the best fit
For some it may help to go back to school and explain the business of polynomials, parabola, coefficients of fit, etc.
Let us start with the basic formula for a parabola, i.e. a polynomial of order 2:

bg(t5) = a2*t52 + a1*t5 + a0

where t5 is the time measured from now and expressed in units of 5 minutes. This definition of t5 makes it very easy to do the sums in the top of the head.
- So, the current t5 is 0 which means bg(0)=a0.
- 5 minutes ago means t5=-1 and bg(-1) = a2-a1+a0 ; etc.

For the deltas we can use the first derivative:

delta(t5) = 2*a2*t5 + a1

resulting in these examples
- currently t5=0 and delta(0) = a1, i.e. the current delta
- 5 minutes ago means t5=-1 and delta(-1) = a1-2*a2 , i.e. the last_delta
- 5 minutes ahead means t5=+1 and delta(1) = a1+2*a2, i.e. the next_delta

For the acceleration we can use the derivative of delta, i.e. the second derivative of bg:

acce (t5) = 2*a2

which is constant.

Best fit after Gauss is a mathemetical formula for a parabola which has minimal square sum of deviations between fitted and real data. With the fit we smooth out noise in the data and need at least 4 measurements to be included. The quality of the fit is measured by the correlation coefficient. AutoISF goes back in BG history and tries increasing the length of the fit window until this correlation coefficient deteriorates.

This gives you the tools to try your own extensions by coding it in VDF. Ideas could be combined effects of delta and acceleration,or long lasting rises like in slope40. I am currently playing with long lasting accelerations, i.e. with parabola_fit_minutes >15.